## Slide 1: Triple Beam Balance and Graduated Cylinder

## Slide 2: A. Triple beam balance
Used to measure MASS

## Slide 3
Pan
Base

## Slide 4: B. How to use
1. Pan needs to be empty
2. All riders are all the way to the left
3. Check if pointer is at zero mark
          If not- Turn adjustment knob slightly
            Too much will BREAK IT

## Slide 5
4. Place object on pan
5. Move 100 g rider first by notches until pointer dips below zero mark
6. Move 100 g rider BACK one notch
7. Now move the 10 g rider
8. Lastly move the 1 g rider until pointer is at zero
OBJECT

## Slide 6: c. Record mass
Add the numbers on the three riders
100 g rider= 0 g
10g rider= 60 g
1g rider= 2.4 g
300
70
3.4
0 + 60 + 2.4= 62.4
300 + 70 + 3.4= 373.4 g

## Slide 7: D. Graduated Cylinder
Used to measure VOLUME
Read the meniscus
  Bottom of curve
  At eye level
6.6mL
52mL
7
7.8 7.6 7.4 7.2 7.0 6.8 6.6 6.4 6.2

## Slide 8: http://www.ohaus.com/input/tutorials/tbb/TBBread.html